## Slide 1: What is Reconfigurable Computing?
  Computation using hardware that can adapt at the logic level to solve specific problems
Why is this interesting?
  Many applications are poorly suited to microprocessors
  VLSI “explosion” provides increasing resources. How can we use them?
    “field-programmable” devices
  Allows for high performance, bug fixes, and fast time-to market for a selection of applications

## Slide 2: What characterizes Reconfigurable Computing?
Parallelism customized to meet design objectives
Logic specialized to perform specific function
Functionality changed as problem requirements change
Parallelism, specialization, hardware-level adaptation

## Slide 3: Microprocessor-based Systems (Temporal)
  Generalized to perform many functions well.
  Operates on fixed data sizes.
  Inherently sequential
    Constrained even with multiple data paths.
Data Storage
(Register File)
ALU
A
B
C
64

## Slide 4: Reconfigurable Computing
  Create specialized hardware for each application.
  Functional units optimized to perform a special task.
Functional
Unit
A
B
H
L
if (A > B) {
H = A;
L = B;
}
else {
H = B;
L = A;
}

## Slide 5: Example: Bubblesort (Spatial)
  Adapt interconnect to problem.
  Take advantage of parallelism.
A
B
H
L
A
B
H
L
A
B
H
L
A
B
H
L
A
B
H
L
Smallest
Largest

## Slide 6: Implementation Spectrum
  ASIC gives high performance at cost of inflexibility.
  Processor is very flexible but not tuned to the application.
  Reconfigurable hardware is a nice compromise.
Microprocessor
Reconfigurable
Hardware
ASIC

## Slide 7: Implementation Spectrum: ASIC VS FPGA
A Field Programmable Gate Array can be seen as the prototyping stage of Application Specific Integrated Circuits: ASICs are very expensive to manufacture, and once it's made there is no going back (as the most expensive fixed cost is the masks [sort of manufacturing "stencil"] and their development). FPGAs are reprogrammable many times, however because of the fact that a generic array of gates is connected to accomplish your goal, it is not optimised like ASICs. Also, FPGAs are natively dynamic devices in that if you power it off, you loose not only the current state but also your configuration. Boards now exist though that add a FLASH chip and/or a microcontroller to load the configuration at startup so this tends to be a less important argument. Both ASICs and FPGAs can be configured with Hardware Description Languages, and sometimes FPGAs are used for the end product. But generally ASICs kick in when the design is fixed.

## Slide 8: Implementation Spectrum: FPGA vs microcontroller
As for the difference between a microcontroller and a FPGA, you can consider a microcontroller to be an ASIC which basically processes code in FLASH/ROM sequentially. You can make microcontrollers with FPGAs even if it's not optimised, but not the opposite. FPGAs are wired just like electronic circuits so you can have truly parallel circuits, not like in a microcontroller where the processor jumps from a piece of code to another to simulate good-enough parallelism. However because FPGAs have been designed for parallel tasks, it's not as easy to write sequential code as in a microcontroller.
For example, typically if you write in pseudocode "let C be A XOR B", on a FPGA that will be translated into "build a XOR gate with the lego bricks contained (lookup tables and latches), and connect A/B as inputs and C as output" which will be updated every clock cycle regardless of whether C is used or not. Whereas on a microcontroller that will be translated into "read instruction - it's a XOR of variables at address A and address B of RAM, result to store at address C. Load arithmetic logic units registers, then ask the ALU to do a XOR, then copy the output register at address C of RAM". On the user side though, both instructions were 1 line of code. If we were to do this, THEN something else, in HDL we would have to define what is called a Process to artificially do sequences - separate from the parallel code. Whereas in a microcontroller there is nothing to do. On the other hand, to get "parallelism" (tuning in and out really) out of a microcontroller, you would need to juggle with threads which is not trivial. Different ways of working, different purposes.

## Slide 9: Implementation Spectrum: FPGA vs ASIC vs microcontroller
In summary:
ASIC VS FPGA: fixed, more expensive for small number of products (cheaper for high volumes),
but more optimised.
ASIC VS microcontroller: certainly like comparing a tool with a hammer.
FPGA VS microcontroller: not optimised for sequential code processing, but can do truly parallel tasks very easily
as well.
Generally FPGAs are programmed in HDL, microcontrollers in C/Assembly
Whenever speed of parallel tasks is an issue, take an FPGA, evolve your design and finally make it an ASIC if it's cheaper to you in the long run (mass production). If sequential tasks are okay, take a microcontroller. I guess you could do an even more application specific IC from this if it's cheaper to you in the long run as well. The best solution will probably be a bit of both.

## Slide 10: Implementation Spectrum

## Slide 11: Motivation: What is an FPGA?
A Field Programmable Gate Array (FPGA) is a Programmable Logic Device(PLD) with higher densities and capable of implementing different functions in a short period of time.

## Slide 12: Motivation: What is an FPGA?
Block RAMs
Block RAMs
Configurable
Logic
Blocks
I/O
Blocks
Block
RAMs
2-D array of logic blocks and flip-flops with programmable interconnections.
Compact design
User can configure
  Intersections between
the logic blocks
  The function of each block

## Slide 13: Motivation: FPGA vs ASIC vs Microcontroller
ASIC VS FPGA: fixed, more expensive for small number of products (cheaper for high volumes), but more optimized.
ASIC VS microcontroller: certainly like comparing a tool with a hammer.
FPGA VS microcontroller: not optimized for sequential code processing, but can do truly parallel tasks very easily as well.
FPGAs =>HDL & Microcontrollers => Assembly/ C (Even in Java/ Python now)
Parallel tasks => FPGA, finally ASIC (mass production).
Sequential tasks => Microcontrollers

## Slide 14: Motivation: General structure of an FPGA

## Slide 15: Motivation: Xilinx Spartan 3 FPGAs

## Slide 16: Motivation: CLB Structure
Notes: The configurable logic block (CLB) contains two slices. Each slice contains two 4-input look-up tables (LUT), carry & control logic and two registers. There are two 3-state buffers associated with each CLB, that can be accessed by all the outputs of a CLB.
Xilinx is the only major FPGA vendor that provides dedicated resources for on-chip 3-state bussing. This feature can increase the performance and lower the CLB utilization for wide multiplex functions. The Xilinx internal bus can also be extended off chip.

## Slide 17: Motivation: CLB Slice Structure
Each slice contains two sets of the following:
  Four-input LUT
    Any 4-input logic function,
    or 16-bit x 1 sync RAM (SLICEM only)
    or 16-bit shift register (SLICEM only)
  Carry & Control
    Fast arithmetic logic
    Multiplier logic
    Multiplexer logic
  Storage element
    Latch or flip-flop
    Set and reset
    True or inverted inputs
    Sync. or async. control
Notes: The configurable logic block (CLB) contains two slices. Each slice contains two 4-input look-up tables (LUT), carry & control logic and two registers. There are two 3-state buffers associated with each CLB, that can be accessed by all the outputs of a CLB.
Xilinx is the only major FPGA vendor that provides dedicated resources for on-chip 3-state bussing. This feature can increase the performance and lower the CLB utilization for wide multiplex functions. The Xilinx internal bus can also be extended off chip.

## Slide 18: Motivation: LUT (Look-Up Table) Functionality
Look-Up tables are primary elements for logic implementation
Each LUT can implement any function of 4 inputs
Notes: A look up table (LUT) is a memory with a one-bit output
that essentially implements a truth table where each input combination generates a certain logic
output. The input combination is referred to as an address. The HDL synthesizer implements an
AND gate or other simple logic function by programming the stored elements in a LUT.

## Slide 19: VHDL
A
B
X
opcode {+, -, AND, OR}
Behavior VHDL: ALU
compnt ALU (A,B,opcode,X)
case opcode
when => opPlus
X <= A + B;
when => opSub
X <= A – B;
when => opAND
X <= A and B;
when => opOR
X <= A or B;
end case;
end component;
ALU
Structural VHDL: ALU
component ALU (A,B,
opcode, X)
addAB(A,B,Xadd);
subAB(A,B,Xsub);
andAB(A,B,Xand);
orAB(A,B,Xor);
4:1mux(opcode,
Xadd,Xor,
Xand,Xor,X);
end component;

## Slide 20: VHDL
A
B
X
opcode {+, -, AND, OR}
A
B
X
addAB
subAB
andAB
orAB
4:1
Mux
opcode {+, -, AND, OR}
2
Xadd
Xsub
Xand
Xor
ALU
ALU
Structural VHDL: ALU
component ALU (A,B,
opcode, X)
addAB(A,B,Xadd);
subAB(A,B,Xsub);
andAB(A,B,Xand);
orAB(A,B,Xor);
4:1mux(opcode,
Xadd,Xor,
Xand,Xor,X);
end component;

## Slide 21: Computation Models
Abstraction that allows
  Reasoning about computation
    Correctness
    Extraction of parallelism
  Transformations for optimization
  Guarantee Properties
FPGA
Memory
CPU

## Slide 22: Computation Models
Abstraction that allows
  Reasoning about computation
    Correctness
    Extraction of parallelism
  Transformations for optimization
  Guarantee Properties
Memory
Function
1
Function
2
Function
4
Function
3

## Slide 23: Computation Models
Abstraction that allows
  Reasoning about computation
    Correctness
    Extraction of parallelism
  Transformations for optimization
  Guarantee Properties
Memory
Function
5
Function
1
Memory
Function
2
Function
3
Function
4
Memory
Memory
Memory

## Slide 24: Mapping Logics to FPGAs
A
B
addAB
X
A
B
xorAB
X
A
B
andAB
X
A
B
orAB
X
0 0
0 1
1 0
1 1
A B X
0
1
1
0
0 0
0 1
1 0
1 1
A B X
0
1
1
0
0 0
0 1
1 0
1 1
A B X
0
0
0
1
0 0
0 1
1 0
1 1
A B X
0
1
1
1
2-input Look Up Tables (LUTs)
FPGA
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
X <= A+B;
X <= A xor B;
X <= A and B;
X <= A or B;

## Slide 25: Mapping Logics to FPGAs
FPGA
LUT
addAB
LUT
LUT
LUT
xorAB
LUT
LUT
LUT
andAB
LUT
LUT
LUT
orAB
LUT
LUT
A
B
addAB
X
A
B
xorAB
X
A
B
andAB
X
A
B
orAB
X
0 0
0 1
1 0
1 1
A B X
0
1
1
0
0 0
0 1
1 0
1 1
A B X
0
1
1
0
0 0
0 1
1 0
1 1
A B X
0
0
0
1
0 0
0 1
1 0
1 1
A B X
0
1
1
1
2-input Look Up Tables (LUTs)
X <= A+B;
X <= A xor B;
X <= A and B;
X <= A or B;

## Slide 26: Reconfigurable Hardware
  Each LUT operates on four one-bit inputs.
  Output is one data bit.
  Can perform any boolean function of four inputs
  2 = 64K functions (4096 patterns)
Look-up table (LUT)
A
B
C
D
Out
A B C D = out
2
4

## Slide 27: Logic Element

## Slide 28: Field-Programmable Gate Array
  Each logic element outputs one data bit.
  Interconnect programmable between elements.
  Interconnect tracks grouped into channels.
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
LE
Logic Element
Tracks

## Slide 29: FPGA Architecture Issues
  Need to explore architectural issues.
  How much functionality should go in a logic element?
  How many routing tracks per channel?
  Switch “population”?
Logic
Element

## Slide 30: In the Beginning - Xilinx XC4000 Cell
  2 4-input look-up tables
  1 3-input look-up table
  2 D flip flops

## Slide 31: In the Beginning - Xilinx XC4000 Routing
25

## Slide 32: Altera Stratix Logic Element

## Slide 33: Altera Stratix Logic Array Blocks (Clusters)

## Slide 34: Design abstractions
specification
behavior
register-
transfer
logic
circuit
layout
English
Executable
program
Sequential
machines
Logic gates
transistors
rectangles
Throughput,
design time
Function units,
clock cycles
Literals,
logic depth
nanoseconds
microns
function
Spec.
level

## Slide 35: High-level Compilers
  Difficult to estimate hardware resources.
  Some parts of program more appropriate for processor (hardware/software codesign).
  Compiler must parallelize computation across many resources.
  Engineers like to write in C rather than pushing little blocks around.
for (i = 0; i<n, i++)
{
c[i] = a[i] + b[i]
}
Some success stories

## Slide 36: Translating a Design to an FPGA
  CAD to translate circuit from text description to physical implementation well understood.
  Most current FPGA designers use register-transfer level specification (allocation and scheduling)
  Same basic steps as ASIC design.
RTL
.
.
C = A+B
.
Circuit
A
B
+
C
Array

## Slide 37: Circuit Compilation
Technology Mapping
Placement
Routing
LUT
LUT
?
Assign a logical LUT to a physical location.
Select wire segments
And switches for
Interconnection.

## Slide 38: Technology Mapping: A Simple Example
FA
A
B
Co
Ci
S
Made of Full Adders
A+B = D
Logic synthesis tool reduces circuit to
SOP form
Co = ABCi + ABCi + ABCi + ABCi
S = ABCi + ABCi + ABCi + ABCi
LUT
Co
Ci
B
A
LUT
S
Ci
B
A

## Slide 39: Processor + FPGA
1. FPGA serves as coprocessor for data
intensive applications – possible project.
Three possibilities
Backplane bus
(e.g. PCI)
Proc
chip
daughtercard
FPGA
chip
FPGA
Proc
2. FPGA serves as embedded computer
for low latency transfer.
“Reconfigurable Functional Unit”

## Slide 40: Processor + FPGA (cont..)
  FPGA logic embedded inside processor.
  A number of problems with 2 and 3.
    Process technology an issue.
    ALU much faster than FPGA generally.
    FPGA much faster than the entire processor.
RF
ALU
FPGA
Processor
3. Processor integration

## Slide 41: Programmable System on a Chip
Specialized hardware is commonly used for compute-intensive applications
  Coprocessors (FPU, graphics, sound, …)
  Accelerator boards (FPGA boards, I/O cards, …)
FPGAs also perform well for many of these apps
Reconfigurable logic in System-On-A-Chip
RAM
FPGA
DSP
CPU
Custom
Logic
Analog
DSP
RAM
CPU
Custom Logic
FPGA

## Slide 42: Dynamic Reconfiguration
  What if I want to exchange part of the design in the device with another piece?
  Need to create architectures and software to incrementally change designs.
  Effectively a “configuration cache”
  Examples: encryption, filtering.
L
L
L
L

## Slide 43: Classifying Reconfiguration
Reconfiguration methodology
Static
Partially static (=partial reconfiguration)
Dynamic

## Slide 44: Types of Reconfiguration
Types of reconfiguration
  Static reconfiguration – application is not running
  Semi-static – different portions of application time-sliced on same hardware fabric
  Dynamic reconfiguration – application modified in response to changing environmental issues
What is reconfigured?
  Processor reconfiguration – customized instruction sets, pipelining, bit width
  Parameter reconfiguration
  Control reconfiguration
Can you think of other applications?